## Slide 1: P5: Policy-driven optimization of P4 pipeline
Anubhavnidhi “Archie” Abhashkumar*, Jeongkeun Leeo, Jean Tourrilhes#, Sujata Banerjee+, Wenfei Wu#, Joon-Myung Kang# and Aditya Akella*
This work was funded by Hewlett Packard Labs and done during internship program
*University of Wisconsin-Madison, o Barefoot Networks, # Hewlett Packard Labs, + VMware

## Slide 2: Reconfigurable pipeline switches
SDN Control Plane
Rule Translator
Stage Z
Stage X
Stage Y
P4 Compiler
Target switch with flexible pipeline
Parser & Table configuration
Programmed Parser
Pipeline stages
Reconfigurable pipeline switches
Notes: Advent of SDN – focus on control plan
Recently flexible, reconfigurable, programmable pipeline switches and P4 language have been introduced
Also pipeline stages: tables packed into pipeline

## Slide 3: Placing P4 tables into switch pipelines
Switch Pipeline
Switch.p4
P4 Tables
egress_nat
l3_rewrite
tunnel_encap
mpls
ipv4_vtep
mac_acl
nat_flow
ip_acl
validate
ipv6_acl
egress_vlan
tunnel_rewrite
ipv4_multicast
Notes: (pipeline concurrency)

## Slide 4: Factors affecting pipeline concurrency (P4 compiler, NSDI 15)
Resource constraints
  TCAM, SRAM etc
Dependency constraints
  Match-action processing of one table affects match-action processing of other
NAT
match:
  ipv4.srcAddr
  ipv4.dstAddr
action:
  modify dstAddr
Firewall
match:
  ipv4.srcAddr
  ipv4.dstAddr
action:
  drop
  no_op
Resource constraints
  TCAM, SRAM etc
Dependency constraints
  Match-action processing of one table affects match-action processing of other
Notes: Resource constraints represent amount of SRAM, TCAM in each pipeline stage
Our focus is on dependency constraints
What is dependency? Match-action processing of one table affects match-action processing of other
Here ip.dst addr

## Slide 5: Why we need small pipeline stages?
Increase routing table size
Room to run additional advanced network functions
Potential increase of switching throughput

## Slide 6: P4 program with 3 features: Tunneling, NAT, Multicast
tunnel
Fields used:
  ipv4.srcAddr
  ipv4.dstAddr
  ………..
ipv4_vtep
Fields used:
  ipv4.srcAddr
  ipv4.dstAddr
  ………..
nat
Fields used:
  nat_metadata
  ipv4.srcAddr
  ipv4.dstAddr
  …………
ipv4_multicast
Fields Used:
  multicast_metadata
  ipv4.dstAddr
  ……….
tunnel_lookup_miss
Fields used:
  ipv4.srcAddr
  ipv4.dstAddr
  ipv4.protocol
  ………..
  All tables have a dependency relationship with every other table

## Slide 7: Impact of table dependency on switch compiler
Table Dependency Graph
Goal:
  Reduce table dependencies using policy-level information
tunnel
ipv4_vtep
nat
ipv4_multicast
tunnel_lookup_miss
STAGE NO | 1 | 2 | 3 | 4 | 5
tunnel
ipv4_vtep
tunnel_lookup_miss
nat
ipv4_multicast
Pipeline Stages
Notes: Since all act on same field, compiler would put them in serial order, hence all in a separate pipeline stage

## Slide 8: Remove unnecessary table dependency
Not all traffic require all features
High-level policies (policy intents) have such information
Management
Management
Finance
Finance
HR
HR
QOS
Tunnel
NAT
Notes: In this slide, we have listed 3 examples

## Slide 9: Detect mutually exclusive features
PGA (SIGCOMM 15) uses label trees to represent tenant-feature relationship
  Sibling nodes are mutually exclusive
Finance
L2 switching, L3 routing,
Tunnel
L2 switching, L3 routing, NAT
HR
L2 switching, L3 routing, QOS, Multicast, ACL
Support
Tenant
L2 switching, L3 routing
LMS (IM 17) generates label tree(s) from various infrastructure data sources (e.g. LDAP, Cloud services, etc.)
Notes: Siblings are mutually exclusive
Traffic belonging to endpoints of a particular tenant will have features belonging to that tenant
two nodes are mutually exclusive and hence features are mutually exclusive
LMS automated process of label tree
Label tree is just one way to derive this
K: Appear PGA and LMS as well when you talk about it

## Slide 10: P5: Generate accurate table dependency graph
tunnel
ipv4_vtep
nat
ipv4_multicast
tunnel_lookup_miss
STAGE NO | 1 | 2 | 3 | 4 | 5
tunnel
ipv4_vtep
tunnel_lookup_miss
nat
ipv4_multicast
Pipeline Stages

## Slide 11: Remove unnecessary features
P4 programmer may not know what features are required in a network
Policy Intent also tells us what features are essential in a switch
Finance
L2 switching, L3 routing, Tunnel
L2 switching, L3 routing, VLAN, NAT
HR
Support
Tenant
L2 switching, L3 routing
L2 switching, L3 routing,
FINANCE
A
C
B
HR
FINANCE
HR
QOS, Multicast, ACL
Remove these features
Notes: Programmer does not know what feature will be required by network
That depends on the traffic that goes through the network
Features exclusive to Support are not required

## Slide 12: Experimental Setup
“switch.p4” from the P4 github repository
It has 129 tables and over 10K LOC
Features supported by this sample switch : L2 switching, L3 routing, Multicast, Tunneling, QOS, etc
Notes: We wanted to use a real-life example
Represents data plane of an L2/L3 switch

## Slide 13
STAGE NO | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
L2
TUNNEL
VLAN
NAT
L3
QOS
MULTICAST
ACL
Original switch pipeline with 8 enabled features
  # of pipeline stages = 10
Notes: Dark shaded regions represent stages occupied by each feature
Arrows represent dependency relationship

## Slide 14
STAGE NO | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Feature Removal: switch pipeline after removing unused features (QOS, Multicast, ACL)
  Reduced # of pipeline stages to 7
L2
TUNNEL
VLAN
NAT
L3
L2
TUNNEL
VLAN
NAT
L3
QOS
MULTICAST
ACL
STAGE NO | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Notes: Dark shaded regions represent stages occupied by each feature
Arrows represent dependency relationship

## Slide 15
L2
TUNNEL
VLAN
NAT
L3
L2
TUNNEL
VLAN
NAT
L3
STAGE NO | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Dependency Reduction : Switch pipeline with Tenant-to-feature mapping
  Reduced # of pipeline stages to 6
Tenant | Common Feature | Exclusive Feature
HR | L2, L3 | VLAN, NAT
Finance |  | TUNNEL
Notes: Dark shaded regions represent stages occupied by each feature
Arrows represent dependency relationship

## Slide 16: Evaluation: Dependency reduction
Three scenarios
  Scenario 1: each feature used by one tenant
  Scenario 2: each feature used by two tenants
  Scenario 3: each feature used by four tenants
By increasing number of tenants that share the same feature, we decrease the number of mutually exclusive features

## Slide 17: Evaluation: Dependency reduction
Chart: No. of Tenants
| 1 | 2 | 4 | 8 | 16
Used by 1 | 12 | 11 | 10 | 8 | 8
Used by 2 | 12 | 12 | 11 | 11 | 9
Used by 4 | 12 | 12 | 12 | 12 | 12
# of pipeline stages as a function of # of tenants
Performance improvement– bottlenecked by large pipeline stage occupying features
  Tunnel has 6 pipeline stages
Maximum of 33% reduction in # of pipeline stages
50% increase in pipeline efficiency
Without our optimization, it takes 12 pipeline stages
Notes: Blue represents scenario 1, orange 2 and gray 3
Without optimization, p4 compiler takes 12 stage which is the upper bound
Because scenario 3 shares many feature, we could not perform better than original p4 compiler
We will not perform worse than P4
Maximum of 33% reduction in terms of stage usage

## Slide 18: Summary
Exploit knowledge of application requirements from high level policy intent to create an efficient programmable switch pipeline
  Generate accurate table dependencies
  Feature removal
Provide up to 50% improvement in pipeline efficiency
Future work involves optimization across multiple pipelines switches
Notes: To minimize total number of pipeline stages traversed by packet traffic

## Slide 19: Thanks
Notes: To minimize total number of pipeline stages traversed by packet traffic

## Slide 20: Backup Slides
Notes: To minimize total number of pipeline stages traversed by packet traffic

## Slide 21: Reconfigurable pipeline switches
SDN Control Plane
Rule Translator
Parser
L3 Routing
ACL
L2 learning
  Populating:
  Installing and
  querying rules
Target switch with fixed pipeline
SDN Control Plane
Rule Translator
Stage Z
Stage X
Stage Y
P4 Compiler
  Populating:
  Installing and
  querying rules
Target switch with flexible pipeline
Parser & Table configuration
  Configuration:
  P4 program
Programmed Parser
Pipeline stages
Fixed pipeline switches
Reconfigurable pipeline switches
Compiler
Notes: Advent of SDN – focus on control plan
Traditional southbound API
Control plane install rules into switch
Through compiler which does rule translation: translate application level to switch level
Fixed pipeline -> fixed Packet processing
# Single or multiple tables => represent network feature
# New feature => new switch version
----------------------------------------------------------------------------
Recently flexible, reconfigurable, programmable pipeline switches and P4 language have been introduced
Also pipeline stages: tables packed into pipeline (pipeline concurrency)

## Slide 22: Placing P4 tables into switch pipelines
Switch Pipeline
Switch.p4
P4 Tables
egress_nat
l3_rewrite
tunnel_encap
mpls
ipv4_vtep
mac_acl
nat_flow
ip_acl
validate
ipv6_acl
egress_vlan
tunnel_rewrite
ipv4_multicast
mpls
ipv4_vtep
ipv4_multicast
mac_acl
nat_flow
validate
ip_acl
ipv6_acl
egress_nat
l3_rewrite
egress_vlan
tunnel_rewrite
tunnel_encap

## Slide 23: Remove unnecessary table dependency
Not all traffic require all features
Examples
  tenant traffic get virtualized by VTEP feature but not management traffic
  management traffic require advanced QoS but not telemetry traffic
  VPN traffic need firewall but not DC internal traffic
High-level policies (policy intents) have such information
Notes: In this slide, we have listed 3 examples

## Slide 24
STAGE NO | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Feature Removal: switch pipeline after removing unused features (QOS, Multicast, ACL)
  Reduced # of pipeline stages to 7
L2
TUNNEL
VLAN
NAT
L3
Notes: Dark shaded regions represent stages occupied by each feature
Arrows represent dependency relationship

## Slide 25
STAGE NO | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Dependency Reduction : Switch pipeline with Tenant-to-feature mapping
  Reduced # of pipeline stages to 6
L2
TUNNEL
VLAN
NAT
L3
Tenant | Common Feature | Exclusive Feature
HR | L2, L3 | VLAN, NAT
Finance |  | TUNNEL
Notes: Dark shaded regions represent stages occupied by each feature
Arrows represent dependency relationship

## Slide 26: Evaluation: Dependency reduction
Maximum of 33% reduction in terms of stage usage
Notes: Maximum of 33% reduction in terms of stage usage