## Slide 1: RoGUE: RDMA over Generic Unconverged Ethernet
Yanfang Le
with Brent Stephens, Arjun Singhvi, Aditya Akella, Mike Swift
Notes: Good afternoon, I am Yanfang

## Slide 2: RDMA Overview
RoCE: a protocol that provides RDMA over a lossless Ethernet network
USER
KERNEL
HARWARE
RDMA
Zero Copy
Application
Application
Buffer
Buffer
Kernel Bypass Protocol Offload
Low Latency, High throughput, Low CPU utilization
Notes: RDMA is a promising approach for high-performance networking. It provides direct access from user-mode, transferring data to and from application buffer. RDMA bypasses expensive system calls, and perform packetization in hardware.
As a results, RDMA has beautiful features of Low Latency, high throughput, and low cpu utilization.
RDMA is originally developed for infiniband network where there is no packet loss. RoCE is a protocol that enables us to run RDMA on ethernet network.

## Slide 3: Priority Flow Control
RoCE assumes Ethernet network to be lossless – achieved by enabling Priority Flow Control (PFC).
Server/Switch
Switch/Server
Pause frame
Notes: RoCE assumes ethernet network to be lossless. It can be achieved by enabling priority flow control, PFC.
The main idea of PFC is that when the queue length exceeds a threshold, the overloaded switch or server, like the right sided switch or server, will send back a pause frame (animate to send the pause frame) to the upstream switch or server, as result of which, the upstream switch or server will continue to send traffic after pausing for a while.

## Slide 4: Motivation
Data center providers are reluctant to enable PFC
  Instead, isolate RDMA traffic and TCP traffic
RDMA has not seen the uptake it deserves
HOL Blocking
Unfairness
Notes: However, PFC suffers from a serious of problems, e.g., deadlock, head of line blocking, and unfairness.
Thus, data center providers are reluctant to enable PFC. Instead, they isolate RDMA traffic and TCP traffic.
As a result, RDMA has not seen the uptake it deserves.

## Slide 5
  Can we run RDMA over generic Ethernet network without any reliance on PFC ?
Notes: Thus, our question is that
“Can we run RDMA over generic Ethernet network without any reliance on PFC ?
”

## Slide 6
  Can we run RDMA over generic Ethernet network without any reliance on PFC ?
RoCE + PFC
Congestion Control
No packet drop
Congestion Control
Retransmission
yet retain low latency, CPU utilization
RoGUE
Notes: To remove PFC, we first should understand which roles that PFC plays in RoCE world.
As both host and switch can generate the pause frames, PFC provides functionality of congestion control.
RoCE+PFC also ensures no packet drop as the network is lossless by enabling PFC.
On the other hand, in our proposed solution called RoGUE, we do congestion control at the end host and recovery from packet drop is achieved by retransmission. Yet we retain low latency and low cpu utilization.

## Slide 7: RoCE Overview
Signal
CPU
RNIC
RDMA APP
Send QUEUE
Receive QUEUE
QP
Verb
Completion QUEUE
Signal
Brake the animations
Notes: Before diving into ROGUE, Let’s first take a look at RDMA terminologies.
To start a connection, RDMA application first creates a send and receive queue pair. The application sends data in form of chunks called as verbs. A verb is posted to the send queue, which hands it down to the RNIC.
Each verb is translated into one or multiple packets by RNIC and sent out.
After all the packets of a verb are sent out of the NIC or RNIC, it receives an ACK from a remote host, the RNIC will generate completion events, which we called it as singal. (animate)

## Slide 8: Where to fix: HW or SW?
Hardware
  Low CPU utilization, Low Latency
  It requires to work with NIC vendor
  Heterogeneous network hardware with non-standard protocol implementation
  Complicates network evolution
Software
  Easy to implement
  Packet level congestion signals are unavailable
  High CPU utilization if per-packet operations
Notes: To implement the congestion control, loss recovery, the main design issue that we face is where to implement the same, Hardware or software.
HW has the benefits of low CPU utilization and low latency.
However, it requires to work with NIC vendor and heterogenous network hardware cannot handle non-standard protocol implementations. In addition, it complicates network evolution.
On the other hand, it is relatively easy to implement in software. The major issue of software implementation is that packet level congestion signals are unavailable and it will cause high CPU utilization if we use per-packet operation to implement a congestion control, like TCP stack.

## Slide 9: RoGUE Overview
CPU
RNIC
Congestion Control
  Congestion Control loop
  CPU-efficient segmenting
Hardware timestamp to measure RTT
Hardware rate limiter to pace packets
Loss Recovery
Hardware retransmission
  Shadow Queue Pair
Notes: RoGUE does judicious labor division between hardware and software for congestion control, flow control and loss recovery. In the later part of the talk, I am going to use the congestion control to congestion control and flow control.
RoGUE puts the congestion control loop and CPU efficient segmenting in software, and use hardware timestamp to measure RTT, and hardware rate limiter to pace packets.
For loss recovery, we developed a novel mechanism called shadow queue pairs to speed up loss recovery time, and we use hardware retransmission to handle rarely dropped packets.
In this talk, I will focus on the congestion control.

## Slide 10: Congestion Signal
Sender
Switch
Receiver
Packets from different flows
ACK
RTT
ACK
RTT
RTT is high, the queue builds up, reduce the sending rate
RTT is low, network is idle, increase the sending rate
Notes: RoGUE takes RTT as congestion signal. Let’s look at how RTT reflects the congestion on the NIC and network.
First animation.
In this case, queuing happens on the sender NIC, switch, and receiver NIC. The RTT for the red packet is shown as the red brace indicated.
Second animation.
In a worst case, the red packet can even be dropped, then the RTT would become infinite large.
Third animation,
In this case, as no queuing in anywhere. The RTT is quite low.
Fourth animation
Thus, the key idea of RTT-based congestion control is that RTT is high, the queue builds up and network is congestion, the sender should reduce the sending rate.
If RTT is low, network is idle, then, we should increase the sending rate.

## Slide 11: CPU Efficient Segmenting
  Two key questions
    How large a verb should RoGUE send?
    How often should the RNIC signaled?
  Small Verb (< 64KB)
      signal every 64KB
      CPU utilization (< 20%)
  Large Verb (>= 64KB)
      chunk, and signal every 64KB.
      CPU utilization (< 10%)
Host
RNIC
RNIC
Verb 1, 2, 3, 4, 5
Verb 6
Signal 1
Verb 6 packets
Signal 3
Signal 2
Notes: As we mentioned before, if we do per-packet verb RTT measurement, we can get frequent feedback about the network but this comes at the cost of high CPU utilization.
Thus, there are two key questions
Animation 3.
    How large a verb should RoGUE send?
    How often should the RNIC signaled?
so as to preserve most of the CPU utilization benefits of RDMA but not sacrifice the ability to respond to congestion.
First animation,
In case of small verbs, we signal once at the end of multiple small verbs to reduce the CPU utilization as shown here.
For verb 1, 2, 3, 4, 5, we only signal one verb.
Second animation,
On the other hand in case of large verbs(verb 6 in figure, we chuck it and signal multiple times for verb 6 to get the more frequent network feedback.
We conduct a quantative experiment and signal every 64 KB in both cases gives us the low CPU utilization.

## Slide 12: RTT measurement
Host
RNIC
RNIC
Verb 1
Verb 2
Verb 1 packets
Verb 2 packets
Signal 1
Signal 2
Send Ack 1
Send Ack 2
Tenc_s1
Tenc_s2
Tstart_s2
Tcomp_s2
Tcomp_s1
Tstart_si =max(
Verb i enqueued,
last packet of Verb i-1 goes out of NIC)
RTTi= Tcomp_si - Tstart_si - bytes/rate_limit
RTT is measured by Hardware timestamp.
Notes: [Circle the point in the slides ]
Next, we discuss how the RTT is measured.
The straghgtforward RTT measurement is the completion time of a verb minus the enqueue time of a verb.
For example, here the rtt from verb 1 is Tcomp_s1 – Tenc_s1 and minus transmission delay.
RoGUE enqueues 2 verbs back to back to avoid NIC starvation . the expected start time of verb 2 is the max of verb2 enqueued and last packet of verb 1 goes out of NIC.
Animation,
In this example, Tstart_s2 is the start time of the verb 2.
Animation,
At last, the RTT is computed as T_completion – T start – seriazation time.
This RTT reflects the queuing delay at the sender and in the network and is measured by the more precise NIC timestamp.

## Slide 13: Congestion Response
Similar to TCP Vegas, and Timely
If congestion window >= 64KB, window-based + rate limiter
If congestion window < 64KB, rate limiter only
Rate limiter is offloaded to RNIC
Notes: Having known the congestion signal measured, the other main component of congestion control is congestion response, i.e., how much sending rate should be reduced/increase based on the measured RTT.
RoGUE’s congestion response is similar to TCP vegas, and Timely. Note that TCP vegas uses window based approach and Timely uses rate based approach.
RoGUE takes a hybrid approach, because we need window to control the number of outstanding segments in the network and also need rate limit traffic to avoid burst of packets within a segment.
The main idea is that if congestion window > 64KB, which is our signaling threshold, we use a window-based + rate limiter.
If congestion window < 64KB, we pace the packets using rate limiter.
To reduce the CPU utilization, RoGUE offloads rate limit by programming RNIC.

## Slide 14: Evaluation
    Mellanox ConnectX-3 Pro 10Gbps RNICs, DCQCN
    Baselines: DCTCP, DCQCN
Notes: We evaluate the RoGUE with Mellanox ConnectX-3 pro 10Gbps RNICs, which has built-in DCQCN.
We compare with DCTCP, which is a widely deployed data center congestion control protocol
and DCQCN, which is the state-of-the-art RDMA congestion control implemented in RNICs.

## Slide 15: Evaluation-Cluster Experiments
    Each of 16 hosts generates 1MB RPC for random destinations and send 1KB RPC once every ten 1MB RPC
Notes: We evaluated RoGUE at large scale where each of 16 hosts generates 1MB RPC for random destinations and send 1KB RPC once every ten 1MB RPC
The take away here is that RoGUE has lowest the flow completion time for Small RPCs and Large RPCs in comparison to DCTCP and DCQCN.
I should say why?

## Slide 16: Evaluation-Congestion Response
Notes: To evaluate RoGUE’s congestion response efficiency and fairness.
We start with one long-running flow being sent in isolation, and then add/remove up to 4 additional flows, one at a time.
The red dotted line indicates a new flow enters and the green dotted line indicates a new flow leaves.
We measure the instantaneous throughput of all the five RoGUE flows averaged over 1s intervals from different clients sharing a congested link to a single server.
The take away is that all the flows are able to get their fair share of the bottleneck link,
And respond quickly to changes in congestion and converge to a new bandwidth share.

## Slide 17: Evaluation-CPU Utilization
Notes: We also evaluate the CPU utilization. We compared RoGUE against with DCTCP and RoCE.
Server Side – RoGUE has low CPU utilization comparable with RoCE.
Client Side – RoGUE has a lower CPU utlization than DCTCP but slightly higher in comparison to RoCE (due to restricting the verb size to 64 KB in RoGUE whereas RoCE uses 1M)
We have carried out extensive evaluation of RoGUE, even at large scale of 40Gbps and different different RDMA transport types. Please refer to our paper for detailed analysis.

## Slide 18: Summary
It is possible to support RoCE without relying on PFC
Judicious division of labor between SW and HW to do the congestion control and retransmission, yet retain a low CPU utilization
RoGUE supports RC and UC transport types of CC
Evaluation results validate that RoGUE has competitive performance with native RoCE